## Slide 1: Cyberpatriot Session VI
Internet Operating System (IOS) Fundamentals

## Slide 2: Agenda
IOS
Cisco Networking Devices
Interfaces
Switching 101
VLANs
Routing 101
Basic IOS Commands

## Slide 3: Agenda
IOS

## Slide 4: IOS – The “Brains Behind The Magic”
Cisco IOS® Software is the world's leading network infrastructure software, delivering a seamless integration of technology innovation, business-critical services, and hardware platform support. Currently operating on millions of active systems, ranging from the small home office router to the core systems of the world's largest service provider networks, Cisco IOS Software is the most widely leveraged network infrastructure software in the world.
Cisco IOS (originally Internetwork Operating System) is software used on Cisco Systems routers and current Cisco network switches. IOS is a software package of routing, switching, internetworking and telecommunications functions integrated into a multitasking operating system.

## Slide 5: Agenda
Cisco Networking Devices

## Slide 6: Cisco Networking Devices (Icons)
Laptop – PC, Mac
Desktop – PC, iMac
Server – Education Application, Facebook,
Smart Device – iPad, iPhone, Galaxy, Etc

## Slide 7: Cisco Networking Devices (Icons)
Network Router = Post Office
Network Switch – Street with Mailboxes
Wireless Access Point – Same as a switch, just no wires!

## Slide 8: Two towns

## Slide 9: Two towns

## Slide 13: Agenda
Interfaces

## Slide 14: Interface Defined
A hardware interface is described by the mechanical, electrical and logical signals at the interface and the protocol for sequencing them (sometimes called signaling).
Think Lock and Key

## Slide 15: Interface Examples
RJ-45
Optical
Serial

## Slide 16: Interfaces – Speeds and Feeds

## Slide 17: Agenda
Switching 101

## Slide 18: Switching 101
Layer 2 switching uses the media access control address (MAC address) from the host's network interface cards (NICs) to decide where to forward frames. Layer 2 switching is hardware based, which means switches use special chips called application-specific integrated circuit (ASICs) to build and maintain filter tables (also known as MAC address tables or Content Addressable Memory or CAM tables).
Network Switch – Neighborhood with Streets and Mailboxes

## Slide 19: Switching 101
Switch
Router
IP Phone
Printer
Mac
PC
Access
Point
iPhone
iPad
Galaxy
Blackberry
Server Farm

## Slide 20: Switching 101
Network Switch – Neighborhood with
Streets and Mailboxes
MFHS Laptop1
MFHS Laptop2

## Slide 21: Agenda
VLANs

## Slide 22: Virtual Local Area Network (VLAN)
A single layer-2 network which is partitioned to create multiple distinct broadcast domains, which are mutually isolated so that packets can only pass between them via one or more routers; such a domain is referred to as a virtual local area network, virtual LAN or VLAN

## Slide 23: Virtual Local Area Network
LAN
VLAN 1
VLAN 2

## Slide 24: Agenda
Routing 101

## Slide 25: Routing 101
A router is a device that forwards data packets between computer networks. It is connected to two or more data lines from different networks and when a data packet comes in one of the lines, the router reads the address information in the packet to determine its ultimate destination. Then, using information in its routing table, it directs the packet to the next network on its journey. Routers perform the "traffic directing" functions on the Internet.
Network Router – Connect the Neighborhoods

## Slide 26: Routing 101
Switch
Router
IP Phone
Printer
Mac
PC
Access
Point
iPhone
iPad
Galaxy
Blackberry
Server Farm
Switch
Router
IP Phone
Printer
Mac
PC
Access
Point
iPhone
iPad
Galaxy
Blackberry
Server Farm
Switch
Router
IP Phone
Printer
Mac
PC
Access
Point
iPhone
iPad
Galaxy
Blackberry
Server Farm
MFHS
HSH
Starbucks
Router
Router
Network Router – Connect the Neighborhoods

## Slide 27: Routing 101
MFHS
HSH
Switch
Server
Switch
Access Point
iPad
Router
G0/0
Router
G0/0.3
G0/1
G0/1

## Slide 28: Agenda
Basic IOS Commands
&
Configuration

## Slide 29: Basic IOS Modes and Commands
? – View available commands
enable – Privileged EXEC Mode
configure terminal – Global Configuration Mode
enable password – Set privileged password
show – View information about specific things on router
exit – Back up one level
end – Exit back to global command line
write memory – Save your configurations
logout
User EXEC Mode
  The default command mode for the CLI is user EXEC mode. The EXEC commands available at the user EXEC level are a subset of those available at the privileged EXEC level. In general, the user EXEC commands allow you to connect to remote devices, change terminal settings on a temporary basis, perform basic tests, and list system information. The prompt for user EXEC mode is the name of the device followed by an angle bracket: Router>.
Privileged EXEC Mode
  Privileged EXEC mode is password protected, and allows the use of all EXEC mode commands available on the system. To enter privileged EXEC mode from user EXEC mode, use the enable command. Privileged EXEC mode allows access to global configuration mode through the use of the enable command. The privileged EXEC mode prompt consists of the devices's host name followed by the pound sign: Router# .
Global Configuration Mode
  Global configuration commands generally apply to features that affect the system as a whole, rather than just one protocol or interface. You can also enter any of the specific configuration modes listed in the following section from global configuration mode.
  To enter global configuration mode, use the configure terminal privileged EXEC command. The router prompt for global configuration mode is indicated by the term config in parenthesis: Router(config)#

## Slide 30: Switch Configuration
enable Privileged EXEC Mode
configure terminal
enable password (ex. Cisco)
hostname (ex. MFHS_Switch) no spaces allowed in hostname
interface (ex. fastethernet 0/1)
description (ex. Connection MFHS Laptop1) any description you wish
ip address (ex. 10.1.2.2 255.255.255.0) ip address and subnet mask
switchport access vlan 2 (ex. Sets port to access only vlan 2) or…
switchport mode trunk (ex. Sets port to trunk all Vlans)
end
write memory (ALAWAYS, ALWAYS, ALWAYS SAVE YOUR WORK)

## Slide 31: Router Configuration
enable Privileged EXEC Mode
configure terminal
hostname (ex. MFHS_Router) no spaces allowed in hostname
interface (ex. gigabit 0/0) and/or…
interface (ex. gigabit 0/0.2 when setting up Vlan Trunk)
description (ex. Connection HSH Router) any description you wish
ip address (10.1.100.1 255.255.255.0) ip address and subnet mask
encapsulation dot1q 2 (ex. Set when trunking vlan 2)
end
write memory (ALAWAYS, ALWAYS, ALWAYS SAVE YOUR WORK)

## Slide 32: End-Point Configuration
Name Your Device (ex. HSH iPad)
IP Address (ex. 10.1.4.100)
Subnet Mask (ex. 255.255.255.0)
Default Gateway (ex. 10.1.4.1)